## Slide 1
FlightRisk NYC
Predicting arrival delay before the aircraft moves
A pre-departure risk model for JFK, LaGuardia and Newark, scored the way an operations desk would actually use it: as a ranked list on a fixed daily alert budget.
DATATHON · NYC Flights 2013 · 336,776 flights
0.507
PR-AUC, held out
24.2%
of all delay minutes reached on a 10% daily budget
0.936
ROC-AUC, cancellations

## Slide 2
Delay is a $33 billion problem
Two thirds of it lands on passengers, not airlines · FAA / NEXTOR Total Delay Impact Study; Airlines for America, DOT Form 41, 2025
$16.7B
borne by passengers each year — lost time, missed connections, unplanned hotels
$8.3B
borne directly by airlines — crew, fuel, maintenance
$98.41
direct operating cost of a single block minute, from the carriers' own DOT filings
The constraint is attention, not information.
A duty manager at a New York airport oversees several hundred departures a day and can meaningfully act on a few dozen — swap an airframe, hold a connection, pre-position a crew. They do not need a better description of yesterday. They need a ranked list early enough to use. That is why this model is evaluated as a rationing device on a fixed daily budget, not as a classifier.

## Slide 3
Almost every published model on this dataset cheats
…and we measured the shortcut instead of taking it
dep_delay — how late the aircraft actually left — sits in the flights table and correlates with arrival delay at ρ ≈ 0.9.
Include it and you get AUC above 0.90. You also get a model that answers a question nobody needs answered: by the time you know dep_delay, the crew is committed, the gate is reassigned, and the passenger with a 55-minute connection is airborne.
Same model, same data, same split
Post-push-back (the usual number)
0.846
Pre-push-back (deployable)
0.507
PR-AUC on the held-out Nov–Dec period
Two thirds of the apparent skill of a “flight delay model” is the observation that the plane left late. The 0.507 is the part that is genuinely forecastable in advance — and it is the whole project.

## Slide 4
What we built
Every stage runs from one command and rebuilds bit-identically
1
Five raw tables
336,776 flights joined to hourly weather, the FAA aircraft registry and airport metadata
2
67 pre-departure features
Leakage-safe by construction; a test suite enforces the boundary, including out-of-fold target encoding
3
Temporal split
Train Jan–Aug, validate Sep–Oct, hold out Nov–Dec. Never random — a random split lets the model peek forward
4
Gradient boosting
40-draw random search per library over forward-chaining folds, then isotonic recalibration
Held out, never touched
PR-AUC (base rate 0.250)
0.507
ROC-AUC
0.716
Precision, riskiest 10% of a day
47%
Cancellation ROC-AUC
0.936
Tier >120 min ROC-AUC
0.793
Metric values identical after a full clean rebuild
1,115 / 1,153

## Slide 5
It has to beat the alternatives, not beat nothing
Share of all delay minutes reached at a 10% daily alert budget, held-out Nov–Dec
Chart: 
| Picking at random | Historical route rate (no ML) | This model
share of delay minutes reached | 0.099796 | 0.14638 | 0.24156
Why this comparison
A desk alerting at random already catches 10% of the delay on a 10% budget. Value has to be stated net of that.
2.4× random · 1.65× the no-ML rule
The budget is spent per day, not pooled — a desk cannot save November's alerts for 22 December. That makes the numbers worse and the exercise real.

## Slide 6
What that is worth
Unit costs cited; mitigation effectiveness assumed pessimistically at 10% and swept from 2% to 40%
$1.81M
airline operating cost avoided over two months
27k
passenger-hours returned ($1.27M at the FAA's $47/hour)
331t
of CO₂ not burned
$1.69M
of it attributable to the model rather than the budget
Break-even sits at 0.11% effectiveness.
Handling an alert costs about $6; the delay it targets is worth about $568. Cost is not what gates this system.
What we cannot measure, we did not assume.
How much of a warned delay a desk actually recovers is not published, and a historical dataset has no counterfactual. So it is swept, not asserted — and this is a ceiling on available value, not a measured saving.

## Slide 7
Then we asked who the alerts actually reach
Ranking by probability is a rationing rule, and it has losers
Chart: 
| EV | B6 | WN | UA | AA | VX
of its late flights, warned about | 0.38176 | 0.2818 | 0.13545 | 0.056619 | 0.038023 | 0.019048
A 36% coverage gap.
Southwest runs late more often than JetBlue and receives a fortieth of the alerts, because the model under-predicts it by 17 points. No AUC would ever show that.
Spending the same budget proportionally cuts the gap from 36% to 6% for 11.6% of the delay caught. Across destination-size quartiles the same change gains 1.3% — there, fairness is free.
Recommendation: budget per carrier, not globally.

## Slide 8
Why you can believe the numbers
Nothing in the prose is taken on trust
✓
Leakage
Scramble every post-departure column and the shipped model's predictions are exactly unchanged. The split is temporal, so a leak would have to travel backwards in time.
✓
Determinism
Delete every artefact, rebuild from the raw CSVs: 1,115 of 1,153 metric values identical, and all 38 that differ are wall-clock timing fields. Booster SHA-256 recorded and checked.
✓
Prose vs artefacts
make verify re-reads every headline number in the report and README from the metrics files and fails on disagreement — including all of the impact and fairness figures.
✓
What we got wrong
A target encoding we had to throw away, a rotation feature that read from the future on the first attempt, and a severity head aimed at the middle instead of the tail. All three are in the report.

## Slide 9
What would come next
Not a bigger model
1
Real forecast weather
A three-hour horizon costs 0.020 PR-AUC using the crudest possible persistence forecast, so today's numbers are a floor. Cheapest available gain.
2
A randomised rollout
Alert on a random half of eligible flights and compare. That measures mitigation effectiveness directly and replaces the one assumption we had to sweep.
3
Beyond three airports
The BTS on-time database has the same schema nationwide, and the inbound-leg blind spot closes as soon as the network is complete rather than NYC-only.
4
Three outcomes, not two
Cancellation is the most predictable outcome in the data at 0.936 ROC-AUC. Production should rank on-time / late / cancelled jointly.
Steps 1 and 4 are code we could write with this dataset. Step 2 is the one that would turn a ceiling into a measurement — and it requires an airline.

## Slide 10
The honest number is the useful one.
0.507, not 0.846. 47% precision per day, not 64% pooled. A ceiling on value, not a measured saving. Every one of those choices made the result look worse and the work mean something.
24.2%
of all delay minutes reached on a 10% daily budget
2.4×
the delay minutes random alerting would reach
$18–19M
available value per year across the three NYC airports
make reproduce · make verify · make app